## Slide 1
NETWORK INFRASTRUCTURE
Secure Multi-VLAN Enterprise Network
Centralized DHCP & DNS • OSPF Routing • SSH Security
VLAN 10
VLAN 20
VLAN 30
VLAN 40
Network Design & Security Project

## Slide 2
01
Project Overview
A scalable routed network with centralized services and secure administration.
4 VLANs
Separate logical networks for VLAN 10, 20, 30 and 40.
Central Services
One DHCP server and one DNS server serve the complete network.
OSPF
Dynamic routing connects all routed networks.
SSH v2
Encrypted remote access replaces Telnet.

## Slide 3
02
Network Topology
Four routers connect the VLAN networks; centralized servers are located in VLAN 10.
Router0
────
Router1
────
Router2
────
Router3
│
VLAN 10 192.168.10.0/24
│
VLAN 20 192.168.20.0/24
│
VLAN 30 192.168.30.0/24
│
VLAN 40 192.168.40.0/24
DHCP Server: 192.168.10.10 | DNS Server: 192.168.10.11

## Slide 4
03
VLAN Addressing Plan
Each VLAN uses its own /24 network and router gateway.
VLAN
Network
Gateway
Role
10
192.168.10.0/24
192.168.10.1
Central Servers
20
192.168.20.0/24
192.168.20.1
Client Network
30
192.168.30.0/24
192.168.30.1
Client Network
40
192.168.40.0/24
192.168.40.1
Client Network

## Slide 5
04
Centralized DHCP
One DHCP server distributes addresses to all four VLANs.
DHCP Server
Static IP 192.168.10.10 Four separate DHCP pools are configured for VLAN 10, 20, 30 and 40.
DHCP REQUEST
↓
ip helper-address
↓
Correct VLAN Pool
DHCP Result
VLAN 10 → 192.168.10.100+ VLAN 20 → 192.168.20.100+ VLAN 30 → 192.168.30.100+ VLAN 40 → 192.168.40.100+

## Slide 6
05
Centralized DNS
All clients receive one common DNS server through DHCP.
DNS SERVER
192.168.10.11
Located in VLAN 10
Distributed by DHCP →
VLAN 10
VLAN 20
VLAN 30
VLAN 40

## Slide 7
06
OSPF Dynamic Routing
OSPF automatically shares routes between the routers.
R0
⇄
R1
⇄
R2
⇄
R3
Area 0 • Dynamic route learning • Inter-VLAN connectivity

## Slide 8
07
Security: SSH Version 2
Secure encrypted remote administration for all routers.
SSH v2
Encrypted communication Local username authentication Secure replacement for Telnet
Configuration
login local transport input ssh show ip ssh
Verification
SSH Enabled version 2.0 Telnet is not accepted on VTY lines.

## Slide 9
08
Testing & Verification
The implementation was tested from clients and through Packet Tracer simulation.
DHCP
PC receives the correct VLAN IP
PING
Communication between VLANs succeeds
DNS
Clients receive 192.168.10.11
SSH
SSH Version 2 is enabled
SIMULATION
Successful PDU confirms end-to-end delivery

## Slide 10
09
Project Outcome
A functional and scalable multi-VLAN network with centralized services and secure administration.
4 VLANs
Logical network segmentation
DHCP
Centralized automatic addressing
DNS
Centralized name resolution
OSPF
Dynamic inter-network routing
SSH v2
Secure remote administration